## Slide 1: Modeling GPU non-Coalesced Memory Access
Michael Fruchtman

## Slide 2: Importance
GPU Energy Efficiency
  Dependent on performance
Complex Memory Model
  Coalesced memory
  Warps of 16 threads
Applications
  Memory bound applications
  Predict the performance

## Slide 3: Goals
Profile the effect of non-coalesced memory access on memory bound GPU applications.
Find a model that matches the delay in performance.
Extend the model to calculate the extra cost in power.

## Slide 4: Coalesced Access
Source: Cuda Programming Guide 3.0

## Slide 5: Coalesced Access
Source: CUDA Programming Guide

## Slide 6: Method and Procedure
Find a memory bound problem
  Matrix/Vector Addition
    8000x8000
  Perform a solution for each level of coalescence
    16 levels of coalescence
    Separate threads from each other
Increasing number of memory accesses
  Same number of instructions
  Increasing memory access time

## Slide 7: Perfect Coalescence
Block Striding

## Slide 8: Example Code
__global__ void matrixAdd(int * A, int * B, int * C, int matrixSize)
{
int startingaddress = blockDim.x * blockIdx.x + threadIdx.x;
int stride = blockDim.x;
for(int currentaddress=startingaddress; currentaddress < matrixSize; currentaddress+=stride)
{
C[currentaddress]=A[currentaddress]+B[currentaddress];
}
}

## Slide 9: Perfect Non-Coalescence
Stream Splitting

## Slide 10: Example Code
__global__ void matrixAdd(int * A, int * B, int * C, int matrixSize)
{
int countperthread = matrixSize/blockDim.x;
int startingaddress=((float)threadIdx.x/blockDim.x)*matrixSize;
int endingaddress = startingaddress+countperthread;
for(int currentaddress=startingaddress; currentaddress<endingaddress; currentaddress++)
{
C[currentaddress]=A[currentaddress]+B[currentaddress];
}
}

## Slide 11: Non-Coalesced Level
Modify Perfect Coalescence Code
  Read the stride from the matrix
  Insert 0s at the right places to stop threads
  Instruction Number
    Slight Increase
    Memory access becomes increasingly non-coalesced
Doesn’t perform perfect matrix addition

## Slide 12: Experimental Setup
Nehalem Processor
  Core i7 920 2.6GHz
  Performance metric included memory transfer
  QPI improves memory transfer performance compared to previous architecture such as Core 2 Duo

## Slide 13: Experimental Setup
NVIDIA CUDA GPU
  EVGA GTX 260 Core 216 896MB
    GT200, CUDA Version 1.3 supports partial coalescence
    Stock speed 576MHz
    Maximum Memory Bandwidth 111.9GB/s
    216 cores in 27 multiprocessors

## Slide 14: Performance
Chart: 
| 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | Perfect 1/16
Performance (milliseconds) | 72.34 | 80.49 | 97.72 | 125.56 | 152.93 | 180.71 | 208.48 | 236.26 | 250.14 | 277.92 | 305.7 | 333.56 | 362.57 | 391.12 | 419.78 | 448.94 | 708.875

## Slide 15: Memory Requested (bytes)
Chart: 
| 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | Perfect 1/16
Memory Requested (Bytes) | 512000000 | 895998976 | 1023993856 | 1279987712 | 1535979520 | 1791969280 | 2047956992 | 2303942656 | 2303942656 | 2559924224 | 2815903744 | 3071864832 | 3327856640 | 3583830016 | 3839801344 | 4095770624 | 4096000000
Memory Stored (Bytes) | 256000000 | 447999488 | 511996928 | 639993856 | 767989760 | 895984640 | 1023978496 | 1151971328 | 1151971328 | 1279962112 | 1407951872 | 1535932416 | 1663928320 | 1791915008 | 1919900672 | 2047885312 | 2048000000

## Slide 16: Instructions Executed
Chart: 
| 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | Perfect 1/16
Instructions Executed | 20000312 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 24000627 | 20000802

## Slide 17: Performance Mystery
Why is perfect non-coalescence so much slower than 1/16 coalescence?
NVIDIA GTX 260 216

## Slide 18: Non-Coalescence Model
Performance is near perfectly linear
  R2 = 0.9966
D(d) =d * Ma
  d: number of non-coalesced memory accesses
  Ma: Memory access time
    Dependent on memory architecture
GT200 Ma= 2.43 microseconds measured
1400 clock cycles

## Slide 19: Model of Extra Power Cost
Power consumption is in a range
Dependent on GPU
  See An Integrated GPU power and performance model
P(d) = D(d) * P(d)
D(d) is delay due to non-coalesced access
P(d) is the average power consumed by GPU while active

## Slide 20: Conclusion
Performance Degrades Linearly with non-coalesced access
  Energy efficiency will also degrade linearly
  Memory-bound applications
GPU Memory Contention
  Switching time between chip significant
Tools to reduce non-coalescence
  CUDA-Lite finds and fixes some non-coalesence

## Slide 21: References and Related Work
NVIDIA. NVIDIA CUDA Programming Guide 3.0. February 20, 2010.
S. Baghsorkhi, M. Delahaye, S. Patel, W. Gropp, W. Hwu. An adaptive performance modeling tool for GPU Architectures. Proceedings of the 15th ACM SIGPLAN symposium on Principles and practice of parallel programming. Volume 45, Issue 5, May 2010.
S. Hong and H. Kim. An integrated GPU power and performance model. Proceedings of the 37th annual international symposium on computer architecture. Volume 38, Issue 3, June 2010.
S. Lee, S. Min, R. Eigenmann. OpenMP to GPGPU: a compiler framework for automatic translation and optimization. Proceedings of the 14th ACM SIGPLAN symposium on Principles and Practice of parallel programming. Volume 44, Issue 4, April 2009.
S. Ueng, M. Lathara, S. Baghsorkhi, W. Hwu. CUDA-Lite: Reducing GPU Programming Complexity. Languages and Compilers for Parallel Computing. Volume 5335, pp. 1-15. 2008.